## Slide 1: Simple Processor: Data Path & Control Unit
Adriando Tavares, Pedro X. Matos

## Slide 2: Outline
Introduction
Data path
Control Unit
Control unit + Data path
Simulation
On real Hardware

## Slide 3: Introduction
This presentation shows you a simple data path and Control Unit of a simple processor;
The circuit was implemented using Verilog Hardware description language;
The simulation will show us the correct behavior of the implemented circuit;
Finaly the circuit will be burned down into your hardware boards;

## Slide 4: Introduction
Verilog
  The Verilog HDL is an IEEE standard hardware description language. It is widely used in the design of digital integrated circuits.
Design Flow

## Slide 5: Introduction
Tool
  Vivado  Logic synthesize
  ISIM simulator  Built-in Vivado  Logic Simulator

## Slide 6: Introduction
Copy the project into your projects folder and then, open the Vivado tool:
Click on, “Open Project”.

## Slide 7: Introduction
Choose the SimpleProcessor project and hit “ok”

## Slide 8: Introduction
Choose the SimpleProcessor project and hit “ok”

## Slide 9: Datapath
Open the datapath.v file and examine it carefully:

## Slide 10: Datapath
What is datapath ?
  is a set of functional units that carry out data required for processing operations.
The datapath presents several control signals that when activated or deactivated in a given clock cycle allow execution of different RT operations
            The execution of an RT operation requires activation or deactivation of each control signals
            The control signals of a datapath are grouped in the so-called control word:
              A single bit is dedicated to each control signal
              Each RT operation is specified by a set of bit in the control word
              Combining several control words in a given sequence, the datapath will perform specific operations in a given order, i.e., execute a program

## Slide 11: Datapath
Control Word | RT Operation | Control Signal | 
 |  | ALoad | Mux
1 | A = A + 3 | 1 | 1
2 | A = B + C | 1 | 0

## Slide 12: Datapath
Control Word | RT Operation | Control Signal | 
 |  | ALoad | Mux
1 | A = A + 3 | 1 | 1
2 | A = B + C | 1 | 0

## Slide 13: Datapath
Control Word | RT Operation | Control Signal | 
 |  | ALoad | Mux
1 | A = A + 3 | 1 | 1
2 | A = B + C | 1 | 0

## Slide 14: Datapath
1 INPUT A
2 IF (A = 5) THEN
3 B = 8
4 ELSE
5 B = 13
6 END IF
7 OUTPUT B
Discuss the implementation of a datapath and control unit for the following algorithm:

## Slide 15: Datapath
Clock
D7-0
Load
4-bits Register A
Clock
Q3-0
D7-0
Load
4-bits Register B
Clock
Q3-0
ALoad
Muxsel
1
0
4
Input
4
‘8’
‘13’
BLoad
4
Output
Out
4
(A=5)
A3
A0
Note that by connecting the comparator output directly to the multiplexer input:
  The datapath generates one state signal less
  And it would be necessary one control signal less
  However, there are cases where timing problems will arise if state signals are used directly to drive some control signals
Control Word | RT Operation | Control Signals |  |  | 
 |  | ALoad | Muxsel | BLoad | Out
1 | INPUT A | 1 | x | 0 | 0
2 | B = 8 | 0 | 1 | 1 | 0
3 | B = 13 | 0 | 0 | 1 | 0
4 | OUTPUT B | 0 | x | 0 | 1
1 INPUT A
2 IF (A = 5) THEN
3 B = 8
4 ELSE
5 B = 13
6 END IF
7 OUTPUT B

## Slide 16: Datapath: interface
How to create in Verilog

## Slide 17: Datapath: internal logic
Control Word | RT Operation | Control Signals |  |  | 
 |  | ALoad | Muxsel | BLoad | Out
1 | INPUT A | 1 | x | 0 | 0
2 | B = 8 | 0 | 1 | 1 | 0
3 | B = 13 | 0 | 0 | 1 | 0
4 | OUTPUT B | 0 | x | 0 | 1

## Slide 18: Datapath: internal logic
Control Word | RT Operation | Control Signals |  |  | 
 |  | ALoad | Muxsel | BLoad | Out
1 | INPUT A | 1 | x | 0 | 0
2 | B = 8 | 0 | 1 | 1 | 0
3 | B = 13 | 0 | 0 | 1 | 0
4 | OUTPUT B | 0 | x | 0 | 1

## Slide 19: Datapath: internal logic
Control Word | RT Operation | Control Signals |  |  | 
 |  | ALoad | Muxsel | BLoad | Out
1 | INPUT A | 1 | x | 0 | 0
2 | B = 8 | 0 | 1 | 1 | 0
3 | B = 13 | 0 | 0 | 1 | 0
4 | OUTPUT B | 0 | x | 0 | 1

## Slide 20: Datapath: internal logic

## Slide 21: Datapath: interface & internal logic

## Slide 22: Control unit
Open the ctrlunit.v file and examine it carefully:

## Slide 23: Control unit
Control Unit
  or in other words a state machine
        Each state corresponds to a control word
        Each state is executed in a clock cycle
        Transitions are dictated by the sequence in which algorithm instructions are executed
        Be aware of (due to implementation with a D flip-flop that changes output at rising edge of the clock):
            At the rising edge of the clock a register is update with new value if the given signal LOAD is enabled
            At each rising edge of the clock, the FSM enters a new state - the next state

## Slide 24: Control unit
S_input
S_not equal
S_equal
S_output
(A5)
(A=5)
Word CTL 1
INPUT A
Word CTL 2
B = 8
Word CTL 4
OUTPUT B
Word CTL 3
B = 13

## Slide 25: Control unit
Gate delay
The control unit want to load data to register A at the first clock
Aload is not change immediately
The register A at the second clock is not collect. (it’s xxx)

## Slide 26: Control unit
Gate delay
The control unit want to load data to register A at the first clock
Aload is not changed immediately

## Slide 27: Control unit
      Control Unit: Building the next state table
          Three registers will be used to encode the five states. For instance:
                (000S_input)
                (001S_extra)
                (010S_notequal)
                (011S_equal)
                (100 S_output)
          Due to noise in the circuit, the FSM can reach one of the unused states (101, 110 or 111). Therefore, we assign the state S_input as the next state from these states
                Another solution would be using don’t care values​​ to simplify the equations of excitement, if it does not matter which is the next state

## Slide 28: Control unit: interface
How to create in Verilog

## Slide 29: Control unit: FSM
FSM : finite state machine
Create FSM for control unit
Assign constant to each state
How to assign binary value to these state in verilog ?
                (000S_input)
                (001S_extra)
                (010S_notequal)
                (011S_equal)
                (100 S_output)

## Slide 30: Control unit
Coding Verilog follow the table
Create FSM as sequential statement
Generate control signal as combination logic
Current State Q2Q1Q0 | Next State Q2nextQ1nextQ0next | 
 | (A=5)’ | (A=5)
(S_input, 000) | (S_extra, 001) | (S_extra, 001)
(S_extra, 001) | (S_notequal, 010) | (S_equal, 011)
(S_notequal, 010) | (S_output, 100) | (S_output, 100)
(S_equal, 011) | (S_output, 100) | (S_output, 100)
(S_output, 100) | (S_output, 100) | (S_output, 100)
(unused, 101) | (S_input, 000) | (S_input, 000)
(unused, 110) | (S_input, 000) | (S_input, 000)
(unused, 111) | (S_input, 000) | (S_input, 000)

## Slide 31: Control unit: next state
Current State Q2Q1Q0 | Next State Q2nextQ1nextQ0next | 
 | (A=5)’ | (A=5)
(S_input, 000) | (S_extra, 001) | (S_extra, 001)
(S_extra, 001) | (S_notequal, 010) | (S_equal, 011)
(S_notequal, 010) | (S_output, 100) | (S_output, 100)
(S_equal, 011) | (S_output, 100) | (S_output, 100)
(S_output, 100) | (S_output, 100) | (S_output, 100)
(unused, 101) | (S_input, 000) | (S_input, 000)
(unused, 110) | (S_input, 000) | (S_input, 000)
(unused, 111) | (S_input, 000) | (S_input, 000)
FSM’s next state

## Slide 32: Control unit: next state
Current State Q2Q1Q0 | Next State Q2nextQ1nextQ0next | 
 | (A=5)’ | (A=5)
(S_input, 000) | (S_extra, 001) | (S_extra, 001)
(S_extra, 001) | (S_notequal, 010) | (S_equal, 011)
(S_notequal, 010) | (S_output, 100) | (S_output, 100)
(S_equal, 011) | (S_output, 100) | (S_output, 100)
(S_output, 100) | (S_output, 100) | (S_output, 100)
(unused, 101) | (S_input, 000) | (S_input, 000)
(unused, 110) | (S_input, 000) | (S_input, 000)
(unused, 111) | (S_input, 000) | (S_input, 000)
FSM’s next state

## Slide 33: Control unit: next state
Current State Q2Q1Q0 | Next State Q2nextQ1nextQ0next | 
 | (A=5)’ | (A=5)
(S_input, 000) | (S_extra, 001) | (S_extra, 001)
(S_extra, 001) | (S_notequal, 010) | (S_equal, 011)
(S_notequal, 010) | (S_output, 100) | (S_output, 100)
(S_equal, 011) | (S_output, 100) | (S_output, 100)
(S_output, 100) | (S_output, 100) | (S_output, 100)
(unused, 101) | (S_input, 000) | (S_input, 000)
(unused, 110) | (S_input, 000) | (S_input, 000)
(unused, 111) | (S_input, 000) | (S_input, 000)
FSM’s next state

## Slide 34: Control unit: next state
Current State Q2Q1Q0 | Next State Q2nextQ1nextQ0next | 
 | (A=5)’ | (A=5)
(S_input, 000) | (S_extra, 001) | (S_extra, 001)
(S_extra, 001) | (S_notequal, 010) | (S_equal, 011)
(S_notequal, 010) | (S_output, 100) | (S_output, 100)
(S_equal, 011) | (S_output, 100) | (S_output, 100)
(S_output, 100) | (S_output, 100) | (S_output, 100)
(unused, 101) | (S_input, 000) | (S_input, 000)
(unused, 110) | (S_input, 000) | (S_input, 000)
(unused, 111) | (S_input, 000) | (S_input, 000)
FSM’s next state

## Slide 35: Control unit: next state
Current State Q2Q1Q0 | Next State Q2nextQ1nextQ0next | 
 | (A=5)’ | (A=5)
(S_input, 000) | (S_extra, 001) | (S_extra, 001)
(S_extra, 001) | (S_notequal, 010) | (S_equal, 011)
(S_notequal, 010) | (S_output, 100) | (S_output, 100)
(S_equal, 011) | (S_output, 100) | (S_output, 100)
(S_output, 100) | (S_output, 100) | (S_output, 100)
(unused, 101) | (S_input, 000) | (S_input, 000)
(unused, 110) | (S_input, 000) | (S_input, 000)
(unused, 111) | (S_input, 000) | (S_input, 000)
FSM’s next state

## Slide 36: Control unit: FSM output
How to implement a control unit output signals in Verilog
Q2Q1Q0 | RT Operation | Control Signal |  |  | 
 |  | ALoad | Muxsel | BLoad | Out
000 | INPUT A | 1 | x | 0 | 0
001 | NOP | 0 | x | 0 | 0
010 | B = 8 | 0 | 1 | 1 | 0
011 | B = 13 | 0 | 0 | 1 | 0
100 | OUTPUT B | 0 | x | 0 | 1
101 | NOP | 0 | x | 0 | 0
110 | NOP | 0 | x | 0 | 0
111 | NOP | 0 | x | 0 | 0
FSM’s output

## Slide 37: Control unit: interface
After synthesizing, we got the control unit module
What are the expected synthesizer outputs ?

## Slide 38: Control unit: internal logic

## Slide 39: Control unit + datapath
Finally, the microprocessor will be build by connecting the control unit to the datapath through control and status signals
(A = 5)
Unit Control
Clock
Reset
ALoad
Muxsel
BLoad
Out
INPUT A
OUTPUT B
ALoad
Muxsel
BLoad
Out
(A = 5)
Datapath
Clock
Reset
Input
4
4
Clock
Reset
Status signal
Control Signals

## Slide 40: Control unit + datapath
Map two modules together:

## Slide 41: Control unit + datapath
Result:

## Slide 42: Simulation
Add the following testbench to your project and then verify its behavior:

## Slide 43: Simulation
Run simulation and observe the outputted waveform:

## Slide 44: Xilinx description file
Check the *.xdc file:

## Slide 45: Bitstream
Create the bitstream and burn it into your Zybo device;
Check the functionality on the hardware;

## Slide 46: Any doubts ????